## Slide 1: NSP Alarms GenAI RCA Agent v4 Using Google Gemini
Rahim Pirbhai
May 2025

## Slide 2: Key Components
Python
  NSP client
  Kafka client
  RCA Agent
NSP
  24.11
  Kafka alarms (Topic= NSP-FAULT-YANG)
LLM
  Google Gemini
    2.0 Flash

## Slide 3: UML

## Slide 4: Anonymized Data
Actual | Sent to LLM
2025-05-12T18:32:02.760893587Z ¦ sim234_225 ¦ fdn:app:mdm-ami-cmodel:2001::225:service:Site:/service[service-id='411'] ¦ Interface toCE is not operational | 2025-05-12T18:32:02.760893587Z ¦ jfr9fge1 ¦ fdn:app:mdm-ami-cmodel:3pifkb1q:service:Site:/service[yo4xz9f0] ¦ avlb8xpc is not operational
2025-05-20T19:49:34.586318210Z ¦ sim234_225 ¦ fdn:app:mdm-ami-cmodel:2001::225:equipment:Equipment:/port[port-id='1/1/c3/1'] ¦ Interface 1/1/c3/1 is not operational | 2025-05-20T19:49:34.586318210Z ¦ jfr9fge1 ¦ fdn:app:mdm-ami-cmodel:3pifkb1q:equipment:Equipment:/port[m0zwciib] ¦ pg8q5tv4 is not operational
2025-05-12T18:32:01.672731026Z ¦ sim234_236 ¦ fdn:app:mdm-ami-cmodel:100.2.3.4:/openconfig-network-instance:network-instances/network-instance/protocols/protocol/bgp/neighbors/neighbor/state:/router[router-name='Base']/bgp/neighbor[ip-address='FFC0:1::1'] ¦ (ASN 200) VR 1: Group iBGP: Peer FFC0:1::1: received notification: code CEASE subcode CONN_REJECT | 2025-05-12T18:32:01.672731026Z ¦ 6cc1vpht ¦ fdn:app:mdm-ami-cmodel:20fwv1o7:/openconfig-network-instance:network-instances/network-instance/protocols/protocol/bgp/neighbors/neighbor/state:/router[router-name='Base']/bgp/neighbor[ip-address='d4by4wp8'] ¦ (zke8kw2c) VR 1: Group iBGP: Peer d4by4wp8: received notification: code CEASE subcode CONN_REJECT
The RCA Agent maintains a dictionary (well-known <-> anonymized) that it builds in real-time.
Identifiers sent to the LLM are garbled; subsequently the anonymized root-cause FDNs that the LLM returns are translated back to their actual well-known values to send to the Actor (the network administrator).
Further anonymization can be achieved by programming the Agent to reset the dictionary periodically (e.g. every 5 minutes) to roll new patterns for the same identifiers.

## Slide 5: RCA Agent Prompt and Output
A few-shot prompt is used
  The following information is sent to LLM:
If there is a single root-cause for the failure: LLM will return a single root-cause FDN
If there are multiple possible root-causes for the failure, LLM will return multiple root-cause FDNs
If there isn’t enough information to make an inference e.g. logical failure in the absence of equipment failure, LLM will return ‘indeterminate’
The next slides show stdout of the Agent working on real-time alarm feeds …
“You are the network alarms RCA agent” | Format of alarms feed (very abbreviated NSP Kafka output in tabular form) |  | How to determine the root-cause failure or failures + expected response format
Two examples of alarm-feeds + expected responses |  | “Explain your reasoning” | 

## Slide 6: RCA Agent ReAct Tools
On-the-fly interactions between the LLM and NSP to clarify per-alarm object identity/association
  Goal: Improve the quality of data sent to the LLM to improve RCA
    Clarify relationships between alarmed objects
      Parent port for L3VPN interface:
      2025-05-20T19:20:18.400111080Z | sim234_225 | fdn:app:mdm-ami-cmodel:2001::225:service:Site:/service[service-id='411'] | Interface toCE is not operational
      IGP NH interface for iBGP peer:
      2025-05-27T17:34:59.819541798Z | sim234_236 | fdn:app:mdm-ami-cmodel:2001::236:/openconfig-network-instance:network-instances/network-instance/protocols/protocol/bgp/neighbors/neighbor/state:/router[router-name='Base']/bgp/neighbor[ip-address='38.120.234.226'] | (ASN 200) VR 1: Group iBGP: Peer 38.120.234.226: received notification: code CEASE subcode CONN_REJECT
      Parent port for PE-CE eBGP peer:
      2025-05-27T17:35:01.972907588Z | sim234_225 | fdn:app:mdm-ami-cmodel:2001::225:/openconfig-network-instance:network-instances/network-instance/protocols/protocol/bgp/neighbors/neighbor/state:/service[service-id='411']/bgp/neighbor[ip-address='10.41.1.2'] | (ASN 200) VR 7: Group toCE: Peer 10.41.1.2: being disabled because the interface is operationally disabled
    Future: Inter-NE correlation (see Future Enhancements section)

## Slide 7: RCA Agent Demo

## Slide 8: RCA Agent Real Output #1
gemini_alarms_rca_agent receiving messages ...
2025-05-20T19:20:18.368294936Z | sim234_225 | fdn:app:mdm-ami-cmodel:2001::225:equipment:Equipment:/port[port-id='1/1/c2/1'] | Interface 1/1/c2/1 is not operational
2025-05-20T19:20:18.400111080Z | sim234_225 | fdn:app:mdm-ami-cmodel:2001::225:service:Site:/service[service-id='411'] | Interface toCE is not operational
2025-05-20T19:20:18.408108809Z | sim234_225 | fdn:app:mdm-ami-cmodel:2001::225:/openconfig-network-instance:network-instances/network-instance/protocols/protocol/bgp/neighbors/neighbor/state:/service[service-id='411']/bgp/neighbor[ip-address='10.41.1.2'] | (ASN 200) VR 7: Group toCE: Peer 10.41.1.2: being disabled because the interface is operationally disabled
🚨root_cause_fdns=["fdn:app:mdm-ami-cmodel:2001::225:equipment:Equipment:/port[port-id='1/1/c2/1']"]🚨
💡reasoning=The alarm 'Interface 1/1/c2/1 is not operational' is an equipment failure. The other alarms are likely caused by this failure. Therefore, the root cause is the interface failure.💡

## Slide 9: RCA Agent Real Output #2
gemini_alarms_rca_agent receiving messages ...
2025-05-20T19:19:00.673005095Z | sim234_236 | fdn:app:mdm-ami-cmodel:2001::236:/openconfig-network-instance:network-instances/network-instance/protocols/protocol/bgp/neighbors/neighbor/state:/router[router-name='Base']/bgp/neighbor[ip-address='38.120.234.226'] | (ASN 200) VR 1: Group iBGP: Peer 38.120.234.226: received notification: code CEASE subcode CONN_REJECT
2025-05-20T19:19:30.674575549Z | sim234_236 | fdn:app:mdm-ami-cmodel:2001::236:/openconfig-network-instance:network-instances/network-instance/protocols/protocol/bgp/neighbors/neighbor/state:/router[router-name='Base']/bgp/neighbor[ip-address='38.120.234.226'] | (ASN 200) VR 1: Group iBGP: Peer 38.120.234.226: received notification: code CEASE subcode CONN_REJECT
🚨root_cause_fdns=['indeterminate']🚨
💡reasoning=The BGP peer received a connection reject notification. This may be due to misconfiguration or an issue with the peer itself. Since there is no indication of a local equipment failure, the root cause is indeterminate.💡

## Slide 10: RCA Agent Real Output #3
gemini_alarms_rca_agent receiving messages ...
2025-05-20T19:49:34.586033743Z | sim234_225 | fdn:app:mdm-ami-cmodel:2001::225:/openconfig-network-instance:network-instances/network-instance/interfaces/interface:/router[router-name='Base']/interface[interface-name='toSR236'] | Interface toSR236 is not operational
2025-05-20T19:49:34.586318210Z | sim234_225 | fdn:app:mdm-ami-cmodel:2001::225:equipment:Equipment:/port[port-id='1/1/c3/1'] | Interface 1/1/c3/1 is not operational
2025-05-20T19:49:34.603975148Z | sim234_225 | fdn:app:mdm-ami-cmodel:2001::225:/openconfig-network-instance:network-instances/network-instance/interfaces/interface:/router[router-name='Base']/interface[interface-name='toSR236'] | BFD: Local Discriminator 49224 BFD session on node 10.225.236.2 is down due to pathDown
2025-05-20T19:49:34.681534008Z | sim234_225 | fdn:app:mdm-ami-cmodel:2001::225:mpls:Mpls:/router[router-name='Base']/mpls | Interface toSR236 is in administrative state: inService, operational state: outOfService
2025-05-20T19:49:34.713502330Z | sim234_225 | fdn:app:mdm-ami-cmodel:2001::225:rsvp:Rsvp:/router[router-name='Base']/rsvp/interface[interface-name='toSR236']/neighbor[ip-address='10.225.236.2'] | Neighbor 10.225.236.2 on interface toSR236 changed to inactive state because linkDown
🚨root_cause_fdns=["fdn:app:mdm-ami-cmodel:2001::225:equipment:Equipment:/port[port-id='1/1/c3/1']"]🚨
💡reasoning=The alarm indicating that interface 1/1/c3/1 is not operational is likely the root cause. This is an equipment failure, and the other alarms related to toSR236 not being operational can be triggered by this.💡

## Slide 11: Target Actor
Which application shall consume the RCA output?
  Enhance NSP FM application?
    New API for Agent to set relationship between alarms:
      ReSTConf (patch/post) API to specify that the root-cause of Alarm X is Alarm Y
  Enhance NBI Kafka for OSS consumption?
    New Kafka topic = NSP-FAULT-RCA-YANG
      An Alarms OSS would subscribe to NSP-FAULT-YANG and NSP-FAULT-RCA-YANG

## Slide 12: Continuous Improvement Slide 1 of 2
v1 -> v2
  Added subscription-monitor daemon
    auto renew-subscription()
      Because NSP subscriptions last for a maximum of 1 hour
v2 -> v3
  Added ReAct tools
  Added logging
  Added MV support (ongoing)
v3 -> v4
  Added support for orphan alarms
    Laying groundwork for joining sliding-windows (see Future Enhancements section)
  Hide Gemini API key

## Slide 13: Continuous Improvement Slide 2 of 2
v4 -> v5
  Added RAG to store vendor/OS/chassis alarms documentation
v5 -> v6
  Added LangGraph to support multi-turn ReAct loops (ongoing)

## Slide 14: Future Enhancements Slide 1 of 3
Current implementation analyzes alarms raised within a sliding 5s window.
  Issue: If a ‘card-down’ failure was reported at the end of the penultimate 5s window, and consequent ‘port-down’ alarms were reported in the next 5s window, the RCA-Agent will correctly identify the ‘card-down’ as the root-cause, but also incorrectly identify the ‘port-down’ alarms as root-causes because the ‘port-down’ alarms are the highest-level alarms in the current window
      Solution: Concatenate alarms from current window with alarms from prior window; perform RCA on the combination
          Assumes that 2 x 5s = 10s window is big enough (it likely is; this will be an improvement over the current single 5s window)
            Additional enhancement: Adjustable window size

## Slide 15: Future Enhancements Slide 2 of 3
Inter-NE alarm correlation e.g.
2025-05-20T19:49:34.586318210Z | sim234_225 | fdn:app:mdm-ami-cmodel:2001::225:equipment:Equipment:/port[port-id='1/1/c3/1'] | Interface 1/1/c3/1 is administratively shutdown
2025-05-20T19:49:34.586412210Z | sim234_225 | fdn:app:mdm-ami-cmodel:2001::225:equipment:Equipment:/port[port-id='1/1/c3/1'] | Interface 1/1/c3/1 is not operational
2025-05-20T19:49:34.606318810Z | sim234_236 | fdn:app:mdm-ami-cmodel:2001::225:equipment:Equipment:/port[port-id='1/1/c3/1'] | Interface 1/1/c3/1 is not operational
🚨root_cause_fdns=["fdn:app:mdm-ami-cmodel:2001::225:equipment:Equipment:/port[port-id='1/1/c3/1']"]🚨
💡reasoning=sim234_225 interface 1/1/c3/1 is down because it is shutdown. Because sim234_225 interface 1/1/c3/1 is physically connected to sim234_236 interface 1/1/c3/1, this likely caused toSR236 interface 1/1/c3/1 to become inoperable.💡

## Slide 16: Future Enhancements Slide 3 of 3
Integrate with Model Context Protocol (MCP)